P20-170

Manufacturer:

PENDOCK, Halesfield 19, Telford, Shropshire, TF7 4QT. 
T: 01952 580590 E: sales@pendock.co.uk W: www.pendock.co.uk

Product Range: 
Pendock Profiles

Product Reference: 
MX 150x300x8mm

Product Description:

The MX range, with a single 90 degree return, is ideal for use at skirting level, ceiling level or vertically at corners to hide cables or pipework. Supplied in pre-formed plywood with white melamine finish

Size:

150mm x 300mm angle section with one 90 degree angle.

Length:

2500mm & 3000mm

Thickness:

8mm

Profile Angle:

90 degrees

Internal Working Space (approx):

142mm x 292mm overall

Finish / Colour:

White Melamine

Jointing:

Butt Joint (see accessories)

Accessories: 
Screws & White Caps

Internal Corners

External Corners

Stop Ends

Butt Joint Covers

Battens

Button Vents (white)

Access Hatches

Drawing References:

MX150x300x8mm