P31-300

Manufacturer:

PENDOCK, Halesfield 19, Telford, Shropshire, TF7 4QT. 
T: 01952 580590 E: sales@pendock.co.uk W: www.pendock.co.uk

Product Range:

Pendock Ducting

Product Reference: 
MCFDT-70x335

Product Description:

FDT floor ducting is designed for use when installing pipework within solid floors to provide a practical, effective and versatile solution that is also aesthetic and allows simple access for maintenance, inspection or pipework repairs.

Size:

70mm deep overall (inc a 12mm plywood cover) x 335mm wide (365mm wide overall inc shoulder flanges)

Length:

2500mm Duct - 2440mm Cover

Thickness:

22 gauge (0.76mm) hot dipped galvanised mild steel tray with 12mm plywood cover as standard

Internal Working Space (approx):

57mm x 110mm minimum x 3 No compartments

Finish / Colour:

hot dipped galvanised mild steel

Jointing:

Butt Joint (see accessories)

Accessories: 
Corners (supplied in 1250mm lengths for site separation and installation)

Tees (supplied in 1250mm lengths for site separation and installation)

Stop Ends

Butt Joint Plates

Risers to skirting board / skirting conduit

Four-way flyovers

British Standards:

Hot dipped galvanised mild steel duct tray to BS 2989: 1982 class Z2

12mm thick decorative plywood cover to BS 1203: 1979

Drawing References:

MCFDT-70x335