P20-170

Manufacturer:

PENDOCK, Halesfield 19, Telford, Shropshire, TF7 4QT.

T: 01952 580590 E: sales@pendock.co.uk W: www.pendock.co.uk

Product Range:

Pendock Radius

Product Reference:

PLY-CL-750

Product Description:

A range of circular pre-formed plywood casing enclosures, using standard components designed to enclose virtually any size of free-standing structural element. They are supplied as pre-finished components fitted with recessed

assembly joints for quick and easy installation. The factory-made sections incorporate aluminium feature joints between the individual components (ref: J3) and all components are joined using assembly joints to achieve a modular and de-mountable enclosure system. The casings are secretly, mechanically fixed to a timber or metal sub-framework system fixed back to the existing structural member.

Size:

750mm Internal (supplied in quadrants)

Length:

Up to 3000mm in one piece as standard; casings can be 'stacked' to achieve heights over 3m.

Thickness:

12mm as standard - Recessed Feature Collars 8mm

Finish / Colour:

Paint Grade;

High Pressure Laminate (HPL);

Real Wood Veneer.

(Bespoke finishes available upon request)

Jointing:

J3 Aluminium Feature Joint (aluminium finish or PPC to any RAL Colour)

J5 Laminated Feature Joint

(Other joint options are available upon request)

Accessories:

(Optional - Internal Framework Components)

(Optional - Recessed Feature Collar for skirting and / or head locations)

(Optional - Removable Panels)

(Optional - Socket / Service Apertures & Patresses)

Fire classifications:

Varies depending upon preferred external surface finish

Drawing References:

PLY-CL-750